HEALTH & SAFETY

Gas Safety Guidelines

1. Introduction……………………………………………………………………………2

2. Emergency Procedures in the Event of a Gas Leak…………………………..….2

3. Carbon Monoxide……………………………………………………….. …………..3

3. Review and Evaluation……………………………………………………………….4

# Introduction

The Gas Safety (Installation and Use) Regulations 1998 (As amended 2018) apply to gas supplies and gas appliances provided for use in all schools.

To meet these requirements Head teachers should ensure that:

- They know where the gas connection should be switched off and how to do it

- All gas appliances are installed by a Gas Safety registered engineer. From the 1st April 2012, all heating engineers fitting gas boilers and water heaters must be qualified in the use of a flue gas analyser. The qualification required is called CPA1 (Combustion Performance Analysis 1), which means that the gas engineer has successfully undertaken training and assessment.

- All fixed gas appliances (e.g. central heating boilers, gas cookers) are tested and inspected at least annually by a Gas Safety registered engineer.

- Gas pipe work soundness test is carried out annually

- Certificates are issued for all tests and inspections carried out to be available in the Building log book

# Gas Leak Emergencies

EMERGENCY PROCEDURES IN THE EVENT OF A GAS LEAK

Do switch off the gas supply Do open all windows and doors Do not switch lights on or off Do not switch electric sockets on or off Do not use naked flames (e.g. matches, lighters) Do not smoke Call the National Grid Emergency Number on 0800 111 999

# Carbon Monoxide

Carbon monoxide (CO) is a colourless, odourless, tasteless, poisonous gas produced by incomplete burning of carbon-based fuels, including gas, oil, wood and coal. Carbon-based fuels are safe to use. It is only when the fuel does not burn properly that excess CO is produced, which is poisonous. When CO enters the body, it prevents the blood from bringing oxygen to cells, tissues, and organs. You can't see it, taste it or smell it but CO can kill quickly without warning. According to the HSE statistics around 20 people die a year from CO poisoning caused by gas appliances and flues that have not been properly installed, maintained or that are poorly ventilated. Levels that do not kill can cause serious harm to health if breathed in over a long period. In extreme cases paralysis and brain damage can be caused as a result of prolonged exposure to CO. Increasing public understanding of the risks of CO poisoning and taking sensible precautions could dramatically reduce this risk.

What preventative measures can I take against carbon monoxide exposure?

- Ensure that any work carried out in relation to gas appliances is to be undertaken by a Gas Safe Registered engineer, competent in that area of work.

- Gas appliances and/or flues are installed and serviced regularly for safety by a Gas Safe Registered engineer.

- Always make sure there is enough fresh air in the room containing the gas appliance.

- If there is a flue or chimney, ensure it is not blocked up and also ensure that vents are not covered.

- If there are appliances that use other fossil fuels, make sure they are serviced and maintained by a competent person.

- It is recommended that audible carbon monoxide (CO) alarms are fitted as a useful back-up precaution but they must not be regarded as a substitute for proper installation and maintenance of gas appliances by a Gas Safe Registered engineer. Before purchasing a CO alarm, always ensure it complies with British Standard EN 50291 and carries a British or European approval mark, such as a Kite mark. CO alarms should be installed, checked and serviced in line with the manufacturer's instructions.

What are the symptoms of carbon monoxide poisoning?

Early symptoms of carbon monoxide (CO) poisoning can mimic many common ailments and may easily be confused with food poisoning, viral infections, flu or simple tiredness. Symptoms to look out for include: tiredness, drowsiness, headaches, giddiness, nausea, vomiting, and pains in the chest, breathlessness, stomach pains, erratic behaviour and visual problems.

For more information visit NHS direct or telephone 111.

If anyone experiences any of the above symptoms and you believe CO may be involved, they must seek urgent medical advice from either your GP or an accident and emergency department. You should ask for a blood or breath test to confirm the presence of CO.

How do you know if you are at risk from carbon monoxide?

Although carbon monoxide (CO) is a colourless, odourless and tasteless gas, signs that indicate incomplete combustion is occurring, resulting in the production of CO, include:

- Yellow or orange rather than blue flames (apart from fuel effect fires or flueless appliances which display this colour flame)

- Soot or yellow/brown staining around or on appliances

- Pilot lights that frequently blow out

- Increased condensation inside windows

What should you do if you think my appliance is spilling carbon monoxide?

- Switch off the appliance and do not reuse until remedial action has been taken

- Shut off the gas supply at the meter control valve (if you know where it is). If gas continues to escape call National Grid on the Gas Emergency Free phone Number 0800 111 999

- Open all doors and windows to ventilate the room

- Visit your GP urgently and tell him/her that you believe your symptoms may be related to carbon monoxide poisoning and request either a blood and/or breath sample

- Contact a Gas Safe Registered engineer to make repairs

# Version Control

| Version Control | Date Released | Approved By | Amendment |
| --- | --- | --- | --- |
| 1 | March 2010 | Health & Safety | Document created. |
| 2 | July 2012 | Health & Safety | Document reviewed with minor changes. |
| 3 | August 2018 | Health & Safety | Document reviewed, NHS number updated, Regs as amended updated. |